## Slide 1
User Experience Study on DASH(1)
Liu Yitong, Liu Hao, Shen Yun, Lin Qi, Shen Hui, Li Yuchen
Beijing university of Posts and Telecommunications, China
Email: liuyitong@bupt.edu.cn
BUPT-QUALCOMM Joint Research Program
Summary
Study on QoE of DASH
  Validate DASH service QoE model
    Research 3 impairment factors on DASH service: Initial Delay, Stall, and Level Variation
    Test 107 video samples and 64 participants
    Propose QoE model in 2 ways: non-linear regression and machine learning
    Compare BUPT model with UCSD model provided by Qualcomm
  Propose a QoE model of level variation
    Identify QoE influence factors via two-way ANOVA analysis
    Propose a QoE evaluation model based on Primacy and Recency Effects
  Predict stall of DASH service
Research on bitrate adaptation algorithms of DASH
  Propose a QoE-based bitrate adaptation algorithm
  Propose a bandwidth estimating method for 2 typical scenarios
  Research on the performance of bitrate adaptation for multi-user scenario
Background
Figure 1. Medium Motion Videos (BunnyCartoon and Movie)
Figure 2. High Motion Videos (Sports)
Video | Amount | Motion | Test Factors
BunnyCartoon_Stall_1-11 | 11 | Medium | Stall
Movie_Case01-48 | 48 | Medium | All factors*
Sport_Case01-48 | 48 | High | All factors
All factors*: stall, initial delay, and level variation
R = f(IID, IST, ILV)
64 participants from BUPT are divided into 3 groups.
Each tester watches about 45 test video clips in one hour.
Impairment due to Level Variation
Impairment due to Initial Delay
Impairment due to Stall
Stall prediction
Figure 1. Buffer under gradually drop scenario
[1] Dongeun Suh et al, "QoE-enhanced Adaptation Algorithm over DASH for Multimedia Streaming" 2014
: estimated bandwidth
: Buffer of client in second
: duration of one segment
:bitrate of level l
:Playback threshold
Predict stall
  1.Stall probability:
Segment size(bytes) obeys Gaussian Distribution:
  Stall occurs when
  Thus
  with
  2.Stall duration
Bitrate Variation
Impairment on bitrate fluctuation pattern
Primacy and Recency Effects
Impairment on bitrate switching
Frequency bitrate decreased switching causes serious subjective impairment
QoE evaluation model for DASH
QoE evaluation functions:
Performance analysis
    35 test videos from both simulated environment and real network traces
    Two-fold cross validation
    Pearson Correlation Coefficient = 0.92
    RMSE = 0.14
    Our QoE model can reflect user’s experience on DASH accurately
Videos provided by Qualcomm

## Slide 2
User Experience Study on DASH(2)
Liu Yitong, Liu Hao, Shen Yun, Lin Qi, Shen Hui, Li Yuchen
Beijing university of Posts and Telecommunications, China
Email: liuyitong@bupt.edu.cn
BUPT-QUALCOMM Joint Research Program
Test Impairment Factors on DASH Service
Polynomial Model
Machine Learning Model
>25.5
≤16.5
>25.5
≤25.5
>16.5
≤16.5
>12.5
≤12.5
Machine Learning Model
Train M5P and Regression Tree.
Regression Tree Model:
PCC : 0.8719, MSE : 0.0961
Performance is improved, even better in low motion scenario.
Result of UCSD Model
(Provided by UCSD)
PCC : 0.91
MSE : 0.082
Our Validation Result of UCSD Model
PCC : 0.7811
MSE : 0.1821
Performance of BUPT Model
Performance Validation of UCSD Model
Subjective Impairment Tests
Subjective impairment tests under simulated environment
    Influence factors:
    Average bitrate
    Bitrate fluctuation patterns:
    Concave, Falling, Convex
    Irregular: bitrate switches frequently with huge amplitude
    Bitrate switching frequency
Estimate bandwidth for 2 typical scenario
  Long-term variation within wide range—response quickly
  Short-term fluctuation within narrow band—keep stable
Bandwidth estimation
Research on multi-user scenario
Figure 2. Bandwidth estimation for scenario 1
Figure 3. Bandwidth estimation for scenario 2
Simulate two-users condition
Compare several bitrate adaptation algorithms
  When bitrate adaptation is smoother , fairness and efficiency are less
Figure 4. User = 2, smooth window size = 1
Unfairness = 545.9; Utilization = 0.819
Figure 5. User = 2, smooth window size = 15
Unfairness = 784.3; Utilization = 0.712
1.Bandwidth change pattern detect:
and :standard variation and average of last n segments’ throughput
2.Bandwidth estimate:
QoE based bit-rate adaptation
Build a real-time QoE model-equation (1)
Utilize real-time QoE model quantitatively for bitrate adaptation, according to Greedy Algorithm--equation (2)
Maximize QoE when choosing bitrate for segment i
Analysis performance
1.Use UCSD DASH QoE model for simulation
2.Compare with algorithm utilizing QoE model qualitatively
3.Deduce overall optimization with provided bandwidth variation
4.Calculate QoE with the given model
Bandwidth Variation Scenario | QoE Scores (using UCSD) |  | 
 | Proposed Algorithm | Compared Algorithm[1] | Overall Optimization
Fluctuation | 3.7419 | 3.5773 | 3.7705
Gradually drop | 3.8380 | 3.3778 | 3.8405
Dramatically drop | 3.9492 | 3.7343 | 3.9506
Table 1. QoE Comparison

## Slide 3
Rate Adaptation Algorithms for Dynamic Adaptive Streaming over HTTP
Lin Qi, Shen Hui, and Liu Yitong
Beijing University of Posts and Telecommunications, China
Email: shenhui0509@bupt.edu.cn
BUPT-QUALCOMM Joint Research Program
Summary
Propose a QoE based bitrate adaptation algorithm
Propose a bandwidth estimation algorithm for 2 typical scenarios
Research on the bitrate adaptation performance for multi-user scenario
QoE based bit-rate adaptation
Build a real-time QoE model-equation (1)
Utilize real-time QoE model quantitatively for bitrate adaptation, according to Greedy Algorithm--equation (2)
Maximize QoE when choosing bitrate for segment i
Future work
Network-assisted DASH
  Involve network device into adaptation
  Resource allocation for multi-user
Analyze performance
1.Propose a stall prediction method
2.Adopt UCSD DASH QoE model for simulation
3.Compare with algorithm utilizing QoE model qualitatively[1]
4.Compare with overall optimization results deduced from provided bandwidth variation
Bandwidth Variation Scenario | QoE Scores |  | 
 | Proposed Algorithm | Compared Algorithm[1] | Overall Optimization
Fluctuation | 3.7419 | 3.5773 | 3.7705
Gradually drop | 3.8380 | 3.3778 | 3.8405
Dramatically drop | 3.9492 | 3.7343 | 3.9506
Table 1. QoE Comparison
Simulate two-users condition
Compare several bitrate adaptation algorithms
When bitrate adaptation is smoother , fairness and efficiency are less
Figure 4. User = 2, smooth window size = 1
Unfairness = 545.9; Utilization = 0.819
Research on multi-user scenario
Figure 5. User = 2, smooth window size = 15
Unfairness = 784.3; Utilization = 0.712
Note :Smooth window size: The number of segments involved in bandwidth estimation
: estimated bandwidth
: Buffer of client in second
: duration of one segment
:bitrate of level l
:Playback threshold
Figure 1. Buffer under gradually drop scenario
[1] Dongeun Suh et al, "QoE-enhanced Adaptation Algorithm over DASH for Multimedia Streaming" 2014
: includes stall , initial delay and level variation. Details in another poster.
:State of client before sending request of segment i, mainly buffer length
Bandwidth estimation
Figure 2. Bandwidth estimation for scenario 1
Figure 3. Bandwidth estimation for scenario 2
1.Bandwidth change pattern detect:
and :standard variation and average of last n segments’ throughput
2.Bandwidth estimate:
Estimate bandwidth for 2 typical scenario
  Long-term variation within wide range—response quickly
  Short-term fluctuation within narrow band—keep stable
Predict stall
  1.Stall probability:
Segment size(bytes) obeys Gaussian Distribution:
  Stall occurs when
  Thus
  with
  2.Stall duration

## Slide 4
QoE Model of Level Variation
Primacy and Recency Effects
QoE evaluation functions:
Estimate bandwidth for two typical scenario
  Long-term variation within wide range
  Short-term fluctuation within narrow band
Bandwidth Estimation
Figure 2. Bandwidth estimation for scenario 1
Figure 3. Bandwidth estimation for scenario 2
1.Bandwidth change pattern detect:
and :standard variation and average of last n segments’ throughput
2.Bandwidth estimate: