## Slide 1
User Experience Study on DASH
Liu Yitong, Liu Hao, Shen Yun, Lin Qi, Shen Hui, Li Yuchen
Beijing university of Posts and Telecommunications, China
Email: liuyitong@bupt.edu.cn
BUPT-QUALCOMM Joint Research Program
Summary
Study on QoE of DASH
  Validate DASH service QoE model
    Research 3 impairment factors on DASH service: Initial Delay, Stall, and Level Variation
    Test 107 video samples and 64 participants
    Propose QoE model in 2 ways: non-linear regression and machine learning
    Compare BUPT model with UCSD model provided by Qualcomm
  Propose a QoE model of level variation
    Identify QoE influence factors via two-way ANOVA analysis
    Propose a QoE evaluation model based on Primacy and Recency Effects
  Predict stall of DASH service
Research on bitrate adaptation algorithms of DASH
  Propose a QoE-based bitrate adaptation algorithm
  Propose a bandwidth estimating method for 2 typical scenarios
  Research on the performance of bitrate adaptation for multi-user scenario
Extended research: study on HEVC coding
  Reduce complexity for real-time coding
QoE Model of Level Variation
Test Impairment Factors on DASH Service
Polynomial Model
Machine Learning Model
>25.5
≤16.5
>25.5
≤25.5
>16.5
≤16.5
>12.5
≤12.5
Machine Learning Model
Train M5P and Regression Tree.
Regression Tree Model:
PCC : 0.8719, MSE : 0.0961
Performance is improved, even better in low motion scenario.
Result of UCSD Model
(Provided by UCSD)
PCC : 0.91
MSE : 0.082
Our Validation Result of UCSD Model
PCC : 0.7811
MSE : 0.1821
Performance of BUPT Model
Performance Validation of UCSD Model
Primacy and Recency Effects
QoE evaluation functions:
Estimate bandwidth for two typical scenario
  Long-term variation within wide range
  Short-term fluctuation within narrow band
Bandwidth Estimation
Figure 2. Bandwidth estimation for scenario 1
Figure 3. Bandwidth estimation for scenario 2
1.Bandwidth change pattern detect:
and :standard variation and average of last n segments’ throughput
2.Bandwidth estimate:
Subjective Impairment Tests
Subjective impairment tests under simulated environment
    Influence factors:
    Average bitrate
    Bitrate fluctuation patterns:
    Concave, Falling, Convex
    Irregular: bitrate switches frequently with huge amplitude
    Bitrate switching frequency