## Slide 1: User Experience Study on DASH
Liu Yitong, Liu Hao, Shen Yun, Lin Qi, Shen Hui, Li Yuchen
liuyitong@bupt.edu.cn
Wireless Theories and Technologies Lab
Beijing University of Posts and Telecommunications

## Slide 2: Summary
  Build BUPT QoE model of DASH service
  More accurate than UCSD model
  Research impacts of 3 impairment factors on DASH service: Initial Delay, Stall, and Level Variation
  Propose an accurate QoE model considering level variation
  Based on Primacy and Recency Effects
  Identify level variation influence factors: Bitrate Switching, Bitrate Fluctuation Pattern
  Study on QoE-based bitrate adaptation algorithm in DASH service
  Analyze stall probability and duration
  Utilize a real-time QoE model with stall prediction into the bitrate adaptation algorithm
  Select bitrate level to maximize QoE
  Propose a bandwidth estimating method in DASH service
  Consider 2 typical scenarios
  Response quickly for long-term variation and keep stable for short-term fluctuation
  Research on the performance of bitrate adaptation for multi-user DASH（On-going）
DASH QoE Evaluation
DASH User Experience Improvement

## Slide 3: User Experience Impairment Factors on DASH Service
Conclusion
Video | Amount | Motion | Test factors
Bunny Cartoon | 11 | Medium | Stall
Movie Case | 48 | Medium | All factors*
Sport Case | 48 | High | All factors
All factors*: Stall, Initial Delay, and Level Variation
R = f(IID, IST, ILV)
Impairment due to Level Variation
Impairment due to Initial Delay
Impairment due to Stall
Medium motion
High motion
Impairments of Stall and Level Variation is more serious than Initial Delay.(1st row)
Initial Delay is nearly independent with Stall and Level Variation. (2nd and 3rd row)
Initial Delay and Stall Duration follow linear relation with QoE
    More than 2800 votes are received
    Test 107 video samples and 64 participants
Evaluation methodology: Single-Stimulus (SS)
Variation | R | IID | IST | ILV
R | — |  |  | 
IID | 0.234 | — |  | 
IST | 0.001 | 0.327 | — | 
ILV | 0.000 | 0.927 | 0.946 | —
Correlation of impairment factors
Chart: Initial Delay
| 1 | 2 | 3 | 5 | 6 | 7 | 8 | 9 | 11
 | 4.4 | 4.2941 | 4.25 | 4 | 3.9 | 3.7 | 3.6111 | 3.55 | 3.4
Chart: Stall Duration
| 1 | 2 | 3 | 4 | 5 | 6 | 8 | 9 | 11
 | 4.0588 | 4.1176 | 4.05 | 3.7 | 3.4 | 3.65 | 3.1176 | 3.3 | 2.95
*Strong correlation when value <0.05
Guidance by Qualcomm Research: Yinian Mao (SD), Sha Hua (SD), and Ruiming Zheng (BJ)

## Slide 4: Propose QoE Model
BUPT Model
  The best formulation out of 15 basic elementary functions
Performance analysis
PCC : 0.9251 MSE : 0.0536
Performance is improved, even better in low motion scenario.
Result of UCSD Model
(Provided by UCSD)
PCC : 0.91
MSE : 0.082
Our Validation Result of UCSD Model
PCC : 0.7811
MSE : 0.1821
Performance of BUPT Model
Performance Validation of UCSD Model
UCSD Model
Conduct subjective test on Qualcomm’s request
Validate the UCSD model with BUPT subjective results
UCSD model is not accurate in BUPT subjective test
Build a new model based on the observation of 3 impairment factors

## Slide 5: QoE Model for Level Variation
Subjective impairment tests under simulated environment
    Influence factors:
    Average bitrate
    Bitrate fluctuation patterns:
    Concave, Falling, Convex
    Irregular: bitrate switches frequently with huge amplitude
    Bitrate switching frequency
When bandwidth is changeable and insufficient
QoE promotion of DASH
Fluency influences users’ experience greater than image quality
DASH promotes QoE greatly under the congested practical network with changeable throughput
When bandwidth is stable and sufficient enough
    CBR video #24:
    Stall duration = 110s
    Stall number = 6 times
    Sub. Impair. Value = 60
    DASH video #22:
    Stall duration = 0.35ms
    Stall number = 1
    Sub. Impair. Value = 43
    CBR video #14:
    Stall duration = 0.3ms
    Stall number = 1
    Sub. Impair. Value = 27
    DASH video #22:
    Stall duration = 0.3ms
    Stall number = 1
    Sub. Impair. Value = 45

## Slide 6: QoE Model for Level Variation
    35 test videos from both simulated environment and real network traces
    Two-fold cross validation
    PCC= 0.92
    RMSE = 0.14
    Our QoE model can reflect user’s experience on DASH accurately
QoE evaluation functions:
Impairment on bitrate fluctuation pattern
  Based on Primacy and Recency Effects
Impairment on bitrate switching

## Slide 7: Stall Prediction of DASH Service
Segment size (bytes) obeys Gaussian Distribution [1]
Stall probability
Stall duration
Apply (5) into Ref.[2] to get the QoE impairment prediction of Stall
Stall occurs when the unequal (2) fits, i.e. When , a stall will happen.
[1] Dmitri Jarnikov et al, "Client intelligence for adaptive streaming solutions “, 2011
[2] Yao Liu et al,” User Experience Modeling for DASH Video” ,2013
(1)
(2)
(3)
(4)
(5)
: playback threshold
: duration of a segment
: bit-rate of level
(6)
Predicted stall duration:
=2s, =2Mbps, =8s
: estimated bandwidth
: current buffer of client
Notes: : playback threshold
: estimated bandwidth
: current buffer of client
: duration of a segment
: bit-rate of level
〖𝑇𝐻〗_𝑃𝐵 : playback threshold
〖𝐵𝑊〗_𝑒𝑠𝑡: estimated bandwidth
𝐵𝑢𝑓𝑓𝑒𝑟 : current buffer of client
𝜏 : duration of a segment
𝑏_𝑙 : bit-rate of level 𝑙
5不要了

## Slide 8: QoE Based Bitrate Adaptation in DASH
Select bitrate level lselected(i) for requesting segment i, according to:
QoSNet(i) : network condition;
S(i): DASH client state(buffer length.etc);
KPIDASH(i-1): previous KPIs of DASH( stall, initial delay, level variation etc.).
Orient to maximize use experience
An example, utilizing QoE model from [1]
Real-time KPIDASH calculator & QoE model
  ILV (Impairment due to level variation)
  IST (Impairment due to stall number & duration)
  Re-buffering stage:buffer of client becomes empty at segment n, resume playback until M segments downloaded(reach THPB )
  Playback stage:stall prediction in previous page
  IID(Impairment due to initial delay)
[1] Yao Liu et al,” User Experience Modeling for DASH Video” ,2013.

## Slide 9: QoE Based Bitrate Adaptation in DASH
Performance Analyze
Chart: Bandwidth Variation Scenarios
| Fluctuation | Gradually Drop | Dramatically Drop
Compared Algorithm[2] | 3.5773 | 3.3778 | 3.7343
Proposed Algorithm | 3.7419 | 3.838 | 3.9492
Overall Optimization* | 3.7705 | 3.8405 | 3.9506
Compared algorithm: utilizes QoE model in a qualitative method, when bitrate switch-down is needed, smoother switch is preferred. The algorithm consumes buffer for a smoother switch-down.
[2] Dongeun Suh et al, "QoE-enhanced Adaptation Algorithm over DASH for Multimedia Streaming" 2014.
Overall Optimization :
Deduced off-line with awareness of
  1.Size of segment k with bitrate level l
  2. Average bandwidth when download segment k
Determine a combination of bitrate level for each segments
that maximizes QoE score in a specific QoE model.
Model the problem as Combinatorial Optimization.
Solution: (1)DP(optimization with limit condition); (2) Heuristic algorithms(sub-optimization without limit condition).

## Slide 10: Bandwidth Estimation in DASH
Step1: Variation pattern detection
CV(i): Coefficient Variation of last n segments' throughput
S(i): Standard variation of last n segments' throughput
T(i): Average of last n segments' throughput
Step2: Bandwidth computation
The small value of CV (i) reflects a slight fluctuation of throughput or outliers within a short term;
The big value reflects a persistent large variation of available bandwidth.

## Slide 11: Bandwidth Estimation in DASH
2 typical scenarios(compare our method with VLC method)
  Bandwidth estimation with our method
  Long-term variation within a wide range – Response quickly
  Short-term fluctuation within a narrow range – Keep stable
  Bitrate selection with our method
  – Appropriate switch without frequent fluctations
  Buffer with our method
  – Adequate buffer length

## Slide 12: Multi-Users in DASH service (on going)
More practical scenario: multi-users in DASH service environment
Analyze different bitrate adaptation algorithms
  When bitrate adaptation is smoother, fairness and efficiency are less suffers.
Users=2 , smooth window size = 1
Users=2 , smooth window size = 10
Smooth window size: The number of segments which is involved in bandwidth estimation.
Unfairness = 784.3, Utilization = 0.712
Unfairness = 545.9, Utilization = 0.819
Further work:
  Improve fairness and efficiency / Trade off between QoE and fairness
9

## Slide 13
Thank You