## Slide 1: User Experience Study on DASH
Liu Yitong, Liu Hao, Shen Yun,
Lin Qi, Shen Hui, Li Yuchen
liuyitong@bupt.edu.cn
WT&T Lab @ BUPT
北邮、实验室全称

## Slide 2: Summary
  Build BUPT QoE model of DASH service
  Modify UCSD QoE model （more精确的thanucsd）
  Research 3 impairment factors impact on DASH service: Initial Delay, Stall, and Level Variation
  Propose a QoE model of、considering level variation
  集中 on Primacy and Recency Effects to propose more精确qoemodel
  Identify level variation influence factors: Bitrate Switching, Bitrate Fluctuation Pattern
  Study on QoE-based bitrate adaptation algorithm in DASH service
  Analyze stall probability and duration
  Modify real-time QoE model via stall prediction/use a relt qoe model with stal p to bitrate adaptation alg
  Select bitrate level to maximize QoE
  Propose a bandwidth estimating method
  Detect 2 typical scenarios、从什么角度考虑的
  Response quickly for long-term variation and keep stable for short-term fluctuation
  Research on the performance of bitrate adaptation for multi-user DASH（On-going）
DASH QoE Evaluation
DASH User Experience Improvement
Notes: Improve user experience of DASH service

## Slide 3: User Experience Impairment Factors on DASH Service
Conclusion
Video | Amount | Motion | Test factors
Bunny Cartoon | 11 | Medium | Stall
Movie Case | 48 | Medium | All factors*
Sport Case | 48 | High | All factors
All factors*: Stall, Initial Delay, and Level Variation
R = f(IID, IST, ILV)
Impairment due to Level Variation
Impairment due to Initial Delay
Impairment due to Stall
Medium motion
High motion
Impairments of Stall and Level Variation is more serious than Initial Delay.(1st row)
Initial Delay is nearly independent with Stall and Level Variation. (2nd and 3rd row)
Initial Delay and Stall Duration conform to linearity
    More than 2800 votes are received
    Test 107 video samples and 64 participants
Evaluation methodology: Single-Stimulus (SS)
Variation | R | IID | IST | ILV
R | — |  |  | 
IID | 0.234 | — |  | 
IST | 0.001 | 0.327 | — | 
ILV | 0.000 | 0.927 | 0.946 | —
Correlation of impairment factors
Chart: Initial Delay
| 1 | 2 | 3 | 5 | 6 | 7 | 8 | 9 | 11
 | 4.4 | 4.2941 | 4.25 | 4 | 3.9 | 3.7 | 3.6111 | 3.55 | 3.4
Chart: Stall Duration
| 1 | 2 | 3 | 4 | 5 | 6 | 8 | 9 | 11
 | 4.0588 | 4.1176 | 4.05 | 3.7 | 3.4 | 3.65 | 3.1176 | 3.3 | 2.95
*Strong correlation when value <0.05
Guidance by Qualcomm Research: Yinian Mao (SD), Sha Hua (SD), and Ruiming Zheng (BJ)
Notes: Obsvision
相关性 换成P值，加一句解释，不讲

## Slide 4: Propose QoE Model
BUPT Model
  The best formulation out of 15 basic elementary functions.
Performance analysis
PCC : 0.9251 MSE : 0.0536
Performance is improved, even better in low motion scenario.
Result of UCSD Model
(Provided by UCSD)
PCC : 0.91
MSE : 0.082
Our Validation Result of UCSD Model
PCC : 0.7811
MSE : 0.1821
Performance of BUPT Model
Performance Validation of UCSD Model
UCSD Model
Conduct subjective test on Qualcomm’s demand
Validate the UCSD model with BUPT subjective results
UCSD model is not align、not Accurat in the BUPT subjective test
Build a new model on the basis of former conclusion
Notes: : Non-linear Regression

## Slide 5: QoE Model of Level Variation
    Influence factors from the subjective test:
  Average bitrate
  Bitrate switching frequency
  Bitrate fluctuation patterns: Concave, Falling, Convex, Irregular
Impairment on bitrate fluctuation pattern (Ibfp )
  Based on Primacy and Recency Effects
  Evaluation functions of BFP in the posters
Impairment on bitrate switching Isw
  Frequency bitrate decreased switching causes serious subjective impairment
QoE evaluation functions:
Notes:   Irregular: bitrate switches frequently with huge amplitude
QoE dash属于1-5
  35 test videos from both simulated environment and real network traces
  PCC= 0.92, RMSE = 0.14

## Slide 6: Stall Prediction of DASH Service
Segment size (bytes) obeys Gaussian Distribution [1]
Stall probability
Stall duration
Stall’s impairment [2](Modified into real-time form) （说一句话）
Stall occurs when the unequal (2) fits, i.e. When , a stall will happen.
[1] Dmitri Jarnikov et al, "Client intelligence for adaptive streaming solutions “, 2011
[2] Yao Liu et al,” User Experience Modeling for DASH Video” ,2013
(1)
(2)
(3)
(4)
(5)
(6)
: playback threshold
: estimated bandwidth
: current buffer of client
: duration of a segment
: bit-rate of level
(7)
Predicted stall duration:
=2s, =2Mbps, =8s
Notes: : playback threshold
: estimated bandwidth
: current buffer of client
: duration of a segment
: bit-rate of level
5不要了
〖𝑇𝐻〗_𝑃𝐵 : playback threshold
〖𝐵𝑊〗_𝑒𝑠𝑡: estimated bandwidth
𝐵𝑢𝑓𝑓𝑒𝑟 : current buffer of client
𝜏 : duration of a segment
𝑏_𝑙 : bit-rate of level 𝑙

## Slide 7: QoE Based Bitrate Adaptation Algorithm
Performance simulation
*Modify QoE model[1] into real-time form
Select bitrate level lselected(i) for requesting segment i, according to:
QoSNet(i) : network condition;
S(i): DASH client state(buffer length.etc);
KPIDASH(i-1): previous KPIs of DASH( stall, initial delay, level variation etc.).
Orient to maximize use experience
Chart: Bandwidth Variation Scenarios
| Fluctuation | Gradually Drop | Dramatically Drop
Compared Algorithm[2] | 3.5773 | 3.3778 | 3.7343
Proposed Algorithm | 3.7419 | 3.838 | 3.9492
Overall Optimization* | 3.7705 | 3.8405 | 3.9506
[1] Yao Liu et al,” User Experience Modeling for DASH Video” ,2013.
[2] Dongeun Suh et al, "QoE-enhanced Adaptation Algorithm over DASH for Multimedia Streaming" 2014.
[3] Dmitri Jarnikov et al, "Client intelligence for adaptive streaming solutions “, 2011.
*Overall Optimization[3] : theoretical upper bound under a given bandwidth variation scenario.
Notes: 标题 in dash

## Slide 8: Bandwidth Estimation in DASH
2 typical scenarios
  Long-term variation within a wide range – Response quickly.
  Short-term fluctuation within a narrow range – Keep stable.
Step1:Bandwidth pattern detection
: Standard variation of last n segments throughput
: Average of last n segments throughput
Step 2: Bandwidth computation

## Slide 9: Multi-Users in DASH service (on going)
More practical scenario: multi-users in DASH service environment
Analyze different bitrate adaptation algorithms.
  When bitrate adaptation is smoother, fairness and efficiency are less.
Users=2 , smooth window size = 1
Users=2 , smooth window size = 10
Smooth window size: The number of segments which is involved in bandwidth estimation.
Unfairness = 784.3, Utilization = 0.712
Unfairness = 545.9, Utilization = 0.819
Further work:
  improve users fairness and efficiency/Trade off between QoE and fairness

## Slide 10
Thank You